## Slide 1
Forschung kompakt: Windenergie und Wasserstoff zusammen denken
© Infografik: Fraunhofer IWES, Pictogramme: istock kadirkaba
17.06.2025
  —
    Calculation of Adapter to cardan shaft Adapter_Kupplung_20250304.wbpz
      Deepak Petchimuthu

## Slide 2: Adapter to cardan shaft
WEA-RiWa testbench setup
  Connection of cardan shaft to main shaft
  Transfer torque of the drive to the DUT
  Supports the cardan shaft
  Up to 1e6 cycles: 3x DUT’s with up to 300000 rotations

## Slide 3: Adapter to cardan shaft
Geometry
  Outer tube diameter 168,3 mm
    Tube thickness 10 mm
    Additional hole dia 10 mm in the tube

## Slide 4: Adapter to cardan shaft
Bolt flange to main shaft
10x M20 10.9
Stress area: As = 244.8 mm² Stress diameter: ds = 17.65 mm P = 2.5
Pretension (90%,µK/G=0,12) FMmax = 185.8kN FMmin = 185.8kN / 1.4 = 132.7kN
Tightening torque = 592 Nm
Friction µ = 0.2 (steel to steel)

## Slide 5: Adapter to cardan shaft
Mesh
Hex mesh (quadratic)
Average element quality: 0.93
128485 Nodes / 25127 Elements

## Slide 6: Adapter to cardan shaft
Masses added to the Adapter
Mass Adapter Mass cardan shaft Mass bolts
    Half mass of cardan shaft 10x bolts M20x80 & nuts + 20x washer
     47.9 kg  180 kg  3.4 kg

## Slide 7: Adapter to cardan shaft
Boundary conditions
Fatigue case: LC 2 positive and LC 3 negative self weight
Backside fixed
in all cases

## Slide 8: Adapter to cardan shaft
Boundary conditions
Extreme case: LC 4 Max. Torque load 56 kNm
Backside fixed
in all cases

## Slide 9: Adapter to cardan shaft
Fatigue Results LC 2 & 3
Deformation (pretension subtracted)

## Slide 10: Adapter to cardan shaft
Fatigue Results LC 2 & 3
vonMises stress (pretension subtracted)

## Slide 11: Adapter to cardan shaft
Fatigue Results
Principal stress range at tube (LCmax - LCmin)
   33.2MPa < 40 MPa (@2E6 cycles) acc. to DIN EN 1993-1-9:2010-12 table 8.5

## Slide 12: Adapter to cardan shaft
Fatigue Results
Bolt stress range (LC3 - LC2)
   1MPa < 50 MPa (@2E6 cycles) acc. to DIN EN 1993-1-9:2010-12 table 8.1
LC 2
LC 3

## Slide 13: Adapter to cardan shaft
Extreme Results LC 4
Deformation
Sliding at full load!

## Slide 14: Adapter to cardan shaft
Extreme Results LC 4
vonMises stress (pretension subtracted)
Bolt overload at max load!

## Slide 15: Adapter to cardan shaft
Extreme Results LC 4
vonMises stress (pretension subtracted)
   tube stress at 262 MPa < 300 MPa (S355)
   Holes in the tube are not recommended

## Slide 16: Adapter to cardan shaft
Extreme Results LC 4
Bolt stress range (LC4) < 940 MPa?
  Bolts are overloaded at full load because of sliding in contact
Analytical check against sliding
  Minimum pretension FMmin = 185.8kN / 1.4 = 132.7kN per bolt
  Friction coefficient µ = 0.2
  Bolt circle radius rb = 130mm
  Number of bolts nb = 10
  Max. Torque Tmax = FMmin * µ * nb * rb
  Max. Torque Tmax = 132.7kN * 0.2 *10 * 0.13m
  Max. Torque Tmax = 34.5 kNm

## Slide 17: Adapter to cardan shaft
Extreme: Applicable Torque are limited due to bolts
Bolt stress range (LC4) < 940 MPa?
   up to 35 kNm no sliding expected
Contact Status Sticking?
   up to 35 kNm sticking around the bolts
   Max. Torque load of 56 kNm can damage the bolts
Torque: 14 kNm
21 kNm
28 kNm
35 kNm

## Slide 18: Adapter to cardan shaft
Conclusion
Fatigue utilization for 2e6 cycles:
  tube/weld stress range utilization  83%
  Bolt stress range  2%
Extreme (max. Torque = 56 kNm) utilization:
  Tube/weld stress  87% (without holes)
  Bolt stress range  155%  Torquelimit to 35 kNm
  Bolt contact flange sliding  ≈160%  Torquelimit to 35 kNm
Extreme (Torquelimit = 35 kNm) utilization:
  Tube/weld stress  87% (without holes)
  Bolt stress range  ≈100%
  Bolt contact flange sliding  ≈100%
Notes: Gusswelle wurde mit ~17,5kNm abgeschätzt. Wirkungsgrad für Pendel- und Zylinder-rollenlager liegt bei 98-99% und für Kegelrollenlager bei 97-98%.

## Slide 19
Vielen Dank für Ihre Aufmerksamkeit!
  —
© Fraunhofer IWES/Frank Bauer